## Slide 1: Progress towards regional scale carbon monitoring atmospheric validation: Year 2 results for the Northeast Corridor
Approach:
  focus on the Boston-DC megalopolis corridor
    17% of the U.S. population, less than 2% of the land area
  design a measurement network
  develop an atmospheric modeling framework
  High-resolution transport modeling
    Mesoscale atmospheric model (WRF) coupled to Lagrangian particle dispersion model (STILT)
    Verification includes PBL data from lidar profilers (MiniMPL)
  High-resolution CO2 flux model incorporating
    anthropogenic emissions estimates and the
    CASA model (including its 0.5-deg resolution variant)
  Inverse CO2 flux estimates
Objective:
  downscale the current NASA CMS flux products to the regional and local scales pertinent to Monitoring, Reporting, and Verification (MRV)

## Slide 2: Prototype Monitoring, Reporting and Verification System for the Regional Scale: The Boston-DC Corridor
Institutions involved:

## Slide 3: Observation Network Activities
Cross-calibration of Boston and Earth Networks GHG sensors
  Compare measurements using Harvard and Earth Networks calibration gas tanks
  Agreement to within 0.01 – 0.02 ppm
  Completed second round of cross-calibrations in Year 2
GHG tower site on Long Island, NY
  Continuously operating since installation during Year 1
Micro Pulse Lidar (miniMPLs) data acquisition and analysis:
  Boston University (urban location, pre-existing installation)
  Long Island (collocated with new GHG tower, Year 1 installation)
  Lewisburg, PA (collocated with ENI GHG tower, upwind location)
Real-time acquisition of GHG and miniMPL data

## Slide 4: Atmospheric Modeling Framework
Two WRF configurations selected for corridor runs
WRF model performance evaluation (see poster for details)
  Cross-comparison of 3 different configurations (includes earlier Boston-Metro configuration
  Comparison against standard meteorological observations
  Non-standard observations:
    miniMPL PBL height retrievals
    ACARS commercial aircraft profiles: enhancements to WRF postprocessor and WRF-MET evaluation package
WRF-STILT transport computations
  Enhancements for high-resolution emission inventory grids
  Analysis of footprint sensitivity to WRF model configuration
Current Status:
  WRF-STILT footprint computations for Observing network sites completed
    Baseline WRF configuration
    Baseline period: July 2013 – July 2014

## Slide 5: WRF Modeling
Modeling framework: WRF model setup for corridor simulations
  Nested (36km / 12km / 4km / 1.33km resolution) domains
  Inner-most domain includes an urban canopy parameterization

## Slide 6: WRF Modeling
1.33km resolution domain
urban fraction
model terrain height
Urban parameter database (NUDAPT-44)

## Slide 7: STILT-footprints computed at 1km resolution
Artifacts of raw footprints:
time resolution (near-field, strong wind case)
under-sampling (far-field)
1-hour
6-hours (cumulative)
Interpolated/rescaled:
Employ time interpolation in near field, spatial averaging in far field
Fills in gaps, but retains near-field resolution
Far-field averaging length related to ensemble spread and ensemble size

## Slide 8: Flux Modeling Framework
High resolution a priori flux estimates
  Combine sources of information with high spatial and/or temporal resolution
  Include estimates of biogenic fluxes in and near urban areas
Current Status:
  Completed a two-year (2013/2014) dataset at 1 km spatial / 1 hour temporal resolution
  Geographic coverage is for all states within the Washington DC – Boston urban corridor
  Closely related DARTE product is available from TBD DAAC, and documented in PNAS article

## Slide 9: Flux Modeling Framework
Includes 9 separate anthropogenic sectors:
  On-road *
  Human respiration +
  Oil/gas +
  Point sources *
  Off-road *
  Industrial non-point *
  Air/ship *
  Residential *
  Commercial *
  - same category as in Vulcan, + - not in Vulcan
Two alternate biosphere estimates
  CASA-based inventory
    Generated using high-resolution driver fields
  VPRM based inventory

## Slide 10: Flux modeling: FFCO2

## Slide 11: Flux modeling: Biosphere

## Slide 12: Top-Down Inversion Framework
Top-down inversions builds on prior work for estimates of urban-scale methane leaks from Natural Gas distribution network
  Results provided to TBD DAAC
  Documented in PNAS article:
Extended to CO2 emissions for urban corridor
  Boundary condition estimates incorporate vertical gradient information:

## Slide 13: Stakeholder engagement
Presentations/Briefings based on results of Boston Methane study, and during the creation of the bottom-up inventory:
  New England Conference of Public Utility Commissioners
  National Grid
  Boston Bar Association
  City of Boston Environment Department
  Board of Directors for the Boston Metropolitan Planning Organization
  Environmental Defense Fund
Technical contacts with relevant local and state governments
  e.g., extensive cell-phone based traffic flow data was provided by the Boston Metropolitan Planning Organization

## Slide 14: Next steps:
Observing Network
  Continued monitoring of GHG and miniMPL sites
  Incorporate FTS and OCO-2 data into analysis
Modeling Framework
  Extend baseline computation to full 2-year period
  Examine additional WRF configurations
  Flux modeling: refinements of initial baseline estimates
Top-down inversions
  Treatment of boundary conditions
    Use inflow measurements at tower sites, combine with CT vertical gradient information
    consider alternate estimates and/or simultaneous optimization
  Inversion methodologies:
    Linear rescaling
    Bayesian/geo-statistical (with appropriate constraints on dof)
Stakeholder engagement
  Identify and reach out to additional stakeholders (e.g., municipal and state agencies with mitigation plans, RGGI)
  Identify areas of future collaboration with stakeholders
    Provide study results and methodologies
    Identify potential data sources for emission inventories